## Slide 1: AutoCAD 2D_I
Module 2: Geometric Constructions

## Slide 2: Module Objectives:
Draw and bisect a straight line using a compass.
Draw and divide a straight line into any number of equal parts using
a compass.
Bisect any angle between two straight lines without the aid of a protractor.
Construct a hexagon given the length of one side.
Construct a tangent to a point on a circle.
Construct a common tangent to two circle.
Construct radii to blend with curves and straight lines.

## Slide 3: Introduction

## Slide 4: Introduction
“Construction" in Geometry means to draw shapes, angles or lines accurately.
These constructions use mainly compass,
straightedge (i.e. ruler) and a pencil.
This is the "pure" form of geometric construction where no numbers are involved.
While drawing these constructions, you need to use a sharp medium-hard lead (H to 3H).
Draw construction lines extremely light and all
main lines medium to thin but dark.

## Slide 5: Geometric Constructions by using a compass

## Slide 6: Geometric Constructions by using a compass
Bisecting a Straight Line
Bisecting an Angle
Constructing a regular hexagon given one side length.
Tangency
Next

## Slide 7: Bisecting a Straight Line
1. Draw a line AB, and then place the
compass at one end of line
2. Adjust the compass to slightly longer than
half the line length. Draw arcs above and
below the line. Keeping the same compass
width, draw arcs from other end of line.
3. Place ruler where the arcs cross, and draw
the line CD to bisect AB.
See the Figures

## Slide 8: Bisecting a Straight Line
Back

## Slide 9: Bisecting an Angle
An angle bisector divides the angle into two angles with equal measures.
1. Draw any angle CAB
2. Set compasses to any suitable radius with the compass point on point A mark
P & O as shown in Fig. 2.3 b.
3. Using the same radius, draw arcs from the points P & O to intersect at N
4. Draw a line from N to A to bisect the angle CAB.
See the Figures

## Slide 10: Bisecting an Angle
Back

## Slide 11: Constructing a regular hexagon given one side length.
1.Draw a line segment AF with a specific length.
2.Set the compass point on A, and set its width to F. The compass will remain at this setting until the end of the construction process.
3.From points A and F, draw two arcs so that they intersect. Mark this as point O. This is the center of the hexagon's circumcircle.
4.Move the compass to O and draw a circle. This circle will pass through all six vertices.
5. Move the compass on to A and draw an arc across the circle. This is the next vertex ofthe hexagon.
6.Move the compass to this arc and draw an arc across the circle to create the next vertex.
7.Draw a line between each successive pairs of vertices.

## Slide 12: Constructing a regular hexagon given one side length.
Back

## Slide 13: Tangency
Constructing an arc of any radius (x) which is tangent to two circles of radii (r) and (R) and including both.
1. Subtract the radius (r) of the first circle from the required radius (x) and draw an arc from the center O.
2. Subtract the radius (R) of the Second circle from the required radius (x) and draw an arc from the center O to intersect with the first arc at C.
3. Set compasses to required radius (x) and from the center C draw the required arc Fig. 2.5 c.

## Slide 14: Tangency
Back
where (R=30mm , r=20mm , x=80mm, OB=90 mm).

## Slide 15: Practical Tasks

## Slide 16: Practical Tasks
Class Activities
HomeWorks
Next

## Slide 17: Class Activities
Draw the objects shown below in full size using different drawing tools such as compasses, set squares and tee square. Use an A4 sheet to create the drawing with the same layout shown below.
Back
Task 1
Task 2
Task 3

## Slide 18: Class Activity 1
Back

## Slide 19: Class Activity 2
Back

## Slide 20: Class Activity 3
Back

## Slide 21: HomeWorks
Draw the objects shown below in full size using different drawing tools such as compasses, set squares and tee square. Use an A4 sheet for each of the following objects
Task 1
Task 2
Back

## Slide 22: Task 1
Back

## Slide 23: Task 2
Back

## Slide 24: Supplementary resources

## Slide 25: Supplementary resources
1. http://www.mathopenref.com/consthexagon.html
2. http://www.mathsisfun.com/geometry/constructions.html

## Slide 26: The End